## Slide 1: C H A P T E R 4
Radiation Safety and Protection
05.10.2017

## Slide 2: Sources of Radiation Exposure
The general population is exposed to radiation from:
1- Natural Sources
2- Man made Sources

## Slide 3: I -NATURAL RADIATION - All life on earth has evolved in a continuous exposure to natural radiation from: 1. Cosmic 2. Terrestrial sources - An average annual effective dose of about 2.4 mSv worldwide and 3.0 mSv in the United States because of higher radon levels.

## Slide 4: 1- Cosmic Sources - Includes:- 1. Energetic subatomic particles, 2. Photons from the sun & supernova, 3. The particles & photons generated by the interactions of primary cosmic radiation with atoms and molecules of the earth’s atmosphere.

## Slide 5: Cosmic rays

## Slide 6
- Exposure from cosmic radiation is primarily a function of altitude,
- almost doubling with each 2000-meter (m) increase in elevation, because less atmosphere is present to attenuate the radiation.

## Slide 7: - At sea level the exposure from cosmic radiation is about 0.24 mSv per year; - at an elevation of 1600 m (1 mile, the elevation of Denver, Colorado), it is about 0.50 mSv per year. - The global average is 0.4 mSv per year, about 16% of natural exposure.

## Slide 8
2-Terrestrial Sources
Exposure from terrestrial sources comes from:
(a) external sources such as soil and from,
(b) internal sources, including radon and other radionuclides that are inhaled or ingested.

## Slide 9: 2-Terrestrial Sources

## Slide 10
A-External Radiation.
- Exposure from terrestrial sources comes from radioactive nuclides in the soil, primarily potassium 40 and the radioactive decay products of uranium 238 and thorium 232.
- Most of the γ radiation from these sources comes from the top 20 cm of soil.
- The average terrestrial exposure rate is about 0.5 mSv per year, or approximately 20% of the average annual background exposure.

## Slide 11
B-Internal radiation
- Radon. Radon, a decay product in the uranium series, is estimated to be responsible for approximately 52% of the radiation exposure of the world ’s population about (1.2 mSv).
- Radon is a gas (radon 222) that enters homes and buildings and by itself does little harm.

## Slide 12
However, radon decays to form solid products that emit α particles
- These decay products become attached to dust particles that can be inhaled and deposited on the bronchial epithelium in the respiratory tract.
- Exposure to this quantity of radiation may cause as many as 10,000 to 20,000 lung cancer deaths per year in the United States, mostly in smokers.

## Slide 13
Other sources of internal terrestrial exposure
are radionuclides that are taken up from the external environment by ingestion of uranium and thorium.
- The total exposure from ingestion and inhalation other than radon is estimated at 0.3 mSv per year, about 12% of natural-origin exposure.

## Slide 16
II- MAN-MADE RADIATION
Humans have contributed many additional sources of radiation to the environment .

## Slide 17: II- MAN-MADE RADIATION

## Slide 18
These may be categorized into three major groups:
(1) medical diagnosis and treatment,
(2) consumer and industrial products and sources,
and (3) other minor sources.

## Slide 19
1- Medical Diagnosis and Treatment
-This source of exposure contributes the large majority of exposures from man-made sources.
- Although sources in this group include radiation therapy and nuclear medicine, diagnostic medical exposure is the largest contributor, contributing most of this source.
- Dental x-ray examinations are responsible for less than 1% of the average annual exposures from man-made sources.

## Slide 20
2-Consumer and Industrial Products
This group includes: the domestic
water supply, tobacco products,
combustible fuels, dental porcelain,
television receivers, pocket watches,
smoke alarms, and airport inspection systems
& contributes only a small proportion of the total average annual man-made exposure.

## Slide 21
3-Other Man-made Sources
- Individuals who work at medical and dental x-ray facilities, mining or milling or with nuclear weapons are occupationally exposed to additional radiation exposure.
- Another source is the nuclear fallout from the nuclear weapons testing in the 1950s and early 1960s.

## Slide 22
- Nuclear power (which contributes only about 0.01 mSv to the average annual exposure) is another man-made source of particular concern to the public.
-But accidents have occurred, between 1945 and 1987, 284 nuclear reactor accidents, excluding Chernobyl, were reported in several countries.

## Slide 25
DOSE LIMITS
There 2 organization NCRP (National Council on Radiation Protection and Measurements) & ICRP(International Commission on Radiological Protection) .
Dentists and their staff are occupationally exposed workers and are allowed to receive up to 50 mSv of whole-body radiation exposure per year.
The average dose for individuals occupationally exposed in the operation of dental x-ray equipment is far less than the limit: 0.2 mSv, or 0.4% of the allowable exposure.

## Slide 28
Reducing Dental Exposure
- There are three guiding principles in radiation protection;
- The first is the principle of justification, the dentist must do more good than harm.
-The second guiding rule is the principle of optimization. ALARA
- The third principle is that of dose limitation.

## Slide 29
PATIENT SELECTION CRITERIA
According to (ADA, 2006)
-Dentists should not prescribe routine dental radiographs at preset intervals for all patients. Instead,
- they should prescribe radiographs after an evaluation of the patient ’s needs that includes
a(1) health history
review, a (2)clinical dental history assessment, a (3) clinical examination, and an (4) evaluation of susceptibility to dental diseases